| Horsepower | Project/Where Achieved in Practice | Baseline Engine | Repowered Engine | Emission Reduction |
| --- | --- | --- | --- | --- |
|  |  | Horsepower | Model Year | Horsepower4 | Model Year | EPA Certification Level | Cost ($1,000) | CO | NOx | VOC | SO2 | PM |
| 50 - 99 | Harbor Cruise | 92 (2) | 1985 | 100 (1) | 2005 | Tier 2 | $53 | ND | 65% | 69% | ND | 47% |
| 100 - 174 | Shore Boat | 125 (1) | 1960 | 135 (1) | 2004 | Tier 2 | $20 | ND | 68% | 75% | ND | 57% |
|  | Fishing Boat | 150 (2) | 1978 | 181 (2) | 2004 | Tier 2 | $68 | ND | 63% | 68% | ND | 39% |
|  | Auto Ferry | 150 (1) | 1955 | 180 (1) | 2004 | Tier 2 | $24 | ND | 68% | 75% | ND | 57% |
| 175 - 299 | Passenger | 180 (2) | 1975 | 200 (2) | 2005 | Tier 2 | $89 | ND | 63% | 66% | ND | 39% |
|  | Commercial Fishing | 210 (1) | 1970 | 230 (1) | 2004 | Tier 2 | $40 | ND | 66% | 69% | ND | 49% |
|  | Fishing Boat | 215 (1) | 1975 | 235 (1) | 2004 | Tier 2 | $34 | ND | 63% | 66% | ND | 39% |
|  | Environmental Sampling | 215 (2) | 1977 | 235 (2) | 2004 | Tier 2 | $69 | ND | 63% | 66% | ND | 60% |
|  | Passenger Fishing | 220 (2) | 1967 | 255 (2) | 2004 | Tier 2 | $70 | ND | 68% | 74% | ND | 57% |
|  | Dinner Cruise | 220 (2) | 1958 | 255 (2) | 2004 | Tier 2 | $76 | ND | 68% | 74% | ND | 57% |
|  | Passenger Fishing | 220 (2) | 1960 | 255 (2) | 2004 | Tier 2 | $79 | ND | 68% | 74% | ND | 57% |
|  | Harbor Services | 220 (2) | 1967 | 255 (2) | 2004 | Tier 2 | $77 | ND | 68% | 74% | ND | 71% |
|  | Commercial Diving | 250 (2) | 1973 | 230 (2) | 2004 | Tier 2 | $79 | ND | 63% | 66% | ND | 60% |
|  | Fishing Boat | 270 (1) | 1970 | 330 (1) | 2004 | Tier 2 | $40 | ND | 66% | 69% | ND | 49% |
| Horsepower | Project/Where Achieved in Practice | Baseline Engine | Repowered Engine | Emission Reduction |
|  |  | Horsepower | Model Year | Horsepower4 | Model Year | EPA Certification Level | Cost ($1,000) | CO | NOx | VOC | SO2 | PM |
| 300 - 750 | Small Tug Boat | 300 (2) | 1976 | 330 (2) | 2004 | Tier 2 | $98 | ND | 63% | 66% | ND | 58% |
|  | Commercial Fishing | 320 (1) | 1965 | 255 (1) | 2004 | Tier 2 | $50 | ND | 68% | 74% | ND | 70% |
|  | Commercial Fishing | 320 (1) | 1978 | 330 (1) | 2004 | Tier 2 | $39 | ND | 63% | 66% | ND | 58% |
|  | Research Vessel | 320 (2) | 1968 | 255 (2) | 2004 | Tier 2 | $69 | ND | 68% | 74% | ND | 71% |
|  | Harbor Services | 320 (1) | 1969 | 255 (1) | 2004 | Tier 2 | $39 | ND | 68% | 74% | ND | 70% |
|  | Small Tow Boat | 320 (1) | 1968 | 400 (1) | 2004 | Tier 2 | $43 | ND | 68% | 74% | ND | 70% |
|  | Whale Watching | 325 (2) | 1974 | 450 (2) | 2004 | Tier 2 | $128 | ND | 63% | 66% | ND | 58% |
|  | Passenger Diving/Fishing | 375 (2) | 1976 | 400 (2) | 2004 | Tier 2 | $102 | ND | 63% | 66% | ND | 58% |
|  | Dinner Cruise | 375 (2) | 1977 | 450 (2) | 2004 | Tier 2 | $111 | ND | 63% | 66% | ND | 58% |
|  | Tug Boat | 375 (2) | 1971 | 450 (2) | 2004 | Tier 2 | $128 | ND | 66% | 69% | ND | 65% |
|  | Research | 375 (2) | 1967 | 450 (2) | 2004 | Tier 2 | $128 | ND | 68% | 74% | ND | 70% |
|  | Passenger Fishing | 380 (2) | 1978 | 450 (2) | 2004 | Tier 2 | $102 | ND | 63% | 66% | ND | 58% |
|  | Charter/Excursion Boat | 450 (2) | 1978 | 475 (2) | 2004 | Tier 2 | $142 | ND | 63% | 66% | ND | 58% |
|  | Harbor Cruise | 450 (2) | 1985 | 500 (2) | 2005 | Tier 2 | $225 | ND | 59% | 61% | ND | 58% |
|  | Fishing Boat | 500 (1) | 1990 | 453 (1) | 2004 | Tier 2 | $86 | ND | 45% | 52% | ND | 42% |
| Horsepower | Project/Where Achieved in Practice | Baseline Engine | Repowered Engine | Emission Reduction |
|  |  | Horsepower | Model Year | Horsepower4 | Model Year | EPA Certification Level | Cost ($1,000) | CO | NOx | VOC | SO2 | PM |
| 300 - 750 | Crew Shuttle | 510 (3) | 1979 | 530 (3) | 2004 | Tier 2 | $381 | ND | 63% | 66% | ND | 58% |
|  | Crew/Supply | 520 (2) | 1965 | 450 (2) | 2004 | Tier 2 | $141 | ND | 68% | 74% | ND | 70% |
|  | Crew Boat | 530 (2) | 1979 | 575 (2) | 2004 | Tier 2 | $175 | ND | 63% | 66% | ND | 58% |
|  | Supply/Crew | 550 (3) | 1974 | 600 (3) | 2004 | Tier 2 | $304 | ND | 63% | 66% | ND | 58% |
|  | Supply/Crew | 550 (3) | 1973 | 600 (3) | 2004 | Tier 2 | $304 | ND | 63% | 66% | ND | 58% |
|  | Research & Education | 600 (2) | 1960 | 450 (2) | 2004 | Tier 2 | $139 | ND | 68% | 74% | ND | 70% |
|  | Research | 650 (2) | 1978 | 660 (2) | 2004 | Tier 2 | $245 | ND | 63% | 66% | ND | 58% |

# Footnotes

CARB defined engine power category. See CARB Table B-18, http://www.arb.ca.gov/msprog/moyer/guidelines/2005_Carl_Moyer_Guidelines_Part4.pdf

Specific project or location where engine repower has been achieved in practice.

Emission reduction is from baseline emission rate to specified tier emission rate (all baseline engines are pre Tier 2 - i.e. uncontrolled). For CEQA mitigation purposes, the lowest emission reduction must be used unless greater emission reductions can be demonstrated (e.g. manufacturer guarantee). 
For emission factors see CARB Table B-18, http://www.arb.ca.gov/msprog/moyer/guidelines/2005_Carl_Moyer_Guidelines_Part4.pdf.

All engines are Category 1 type. (1) = number of engines.

For informational purposes only. Cost estimates provided by project proponents. Actual costs may vary. 2004 dollars.

CARB defined engine power category. See CARB Table B-18, http://www.arb.ca.gov/msprog/moyer/guidelines/2005_Carl_Moyer_Guidelines_Part4.pdf

Specific project or location where engine repower has been achieved in practice.

Emission reduction is from baseline emission rate to specified tier emission rate (all baseline engines are pre Tier 2 - i.e. uncontrolled). For CEQA mitigation purposes, the lowest emission reduction must be used unless greater emission reductions can be demonstrated (e.g. manufacturer guarantee). 
For emission factors see CARB Table B-18, http://www.arb.ca.gov/msprog/moyer/guidelines/2005_Carl_Moyer_Guidelines_Part4.pdf.

All engines are Category 1 type. (1) = number of engines.

For informational purposes only. Cost estimates provided by project proponents. Actual costs may vary. 2004 dollars.

CARB defined engine power category. See CARB Table B-18, http://www.arb.ca.gov/msprog/moyer/guidelines/2005_Carl_Moyer_Guidelines_Part4.pdf

Specific project or location where engine repower has been achieved in practice.

Emission reduction is from baseline emission rate to specified tier emission rate (all baseline engines are pre Tier 2 - i.e. uncontrolled). For CEQA mitigation purposes, the lowest emission reduction must be used unless greater emission reductions can be demonstrated (e.g. manufacturer guarantee). 
For emission factors see CARB Table B-18, http://www.arb.ca.gov/msprog/moyer/guidelines/2005_Carl_Moyer_Guidelines_Part4.pdf.

All engines are Category 1 type. (1) = number of engines.

For informational purposes only. Cost estimates provided by project proponents. Actual costs may vary. 2004 dollars.