|  | Emission Reduction |  |
| --- | --- | --- |
| Emission Source | Control Technology (CT) | Date CT Required | CO | NOx | VOC | SO2 | PM | Cost | Project/Where Achieved in Practice |
| Ships, Propulsion Engines | 12-knot speed limit within 20 or 40 nautical miles of Point Fermin | NA | ND | 50% | ND | ND | 0% | Information currently not available. | Within 20 nautical miles is a current POLA and POLB voluntary measure. Within 40 nautical miles is in the Ports’ “Clean Air Action Plan” as Measure SPBP-OGV1 – Vessel Speed Reduction. |
|  | Switching fuel from 2.7% to 1.5% sulfur fuel oil within 40 nautical miles of Point Fermin | NA | 0% | 0% | 0% | 44% | 18% | Annual O&M depends on bunker fuel spot market, and therefore is variable. | POLA and POLB voluntary measure |
|  | Switching fuel from 2.7% to 0.5% sulfur fuel oil within 40 nautical miles of Point Fermin | NA | 0% | 10% | 0% | 81% | 57% | Annual O&M depends on bunker fuel spot market, and therefore is variable . | Information currently not available. |
|  | Emission Reduction |  |
| Emission Source | Control Technology (CT) | Date CT Required | CO | NOx | VOC | SO2 | PM | Cost | Project/Where Achieved in Practice |
| Ships, Propulsion Engines | Switching fuel from 2.7% to 0.2% sulfur fuel oil within 40 nautical miles of Point Fermin | NA | 0% | 0% | 0% | 93% | 65% | Annual O&M depends on bunker fuel spot market, and therefore is variable. | Ports’ Clean Air Action Plan as Measure OGV12. |
| Ships, Propulsion Engines | Selective Catalytic Reduction with low sulfur fuel | NA | 0% | 85% | 0% | 44% | 18% | Retrofit Capital Cost SE: $423,656 ME: $985,144 LE: $2,263,880 New Capital Cost SE: 282,438 ME: $656,763 LE: $1,509,254 Annual O&M SE: $169,400 ME: $427,576 LE: $1,001,500 | Ships in Denmark and Sweden |
|  | Retrofit with slide valves | NA | 0% | 20% | 0% | 0% | 25% | Retrofit Capital Cost SE: $10,920 ME: $36,400 LE: $91,000 | A demonstration project is planned by the California Maritime Working Group |
|  | Emission Reduction |  |
| Emission Source | Control Technology (CT) | Date CT Required | CO | NOx | VOC | SO2 | PM | Cost | Project/Where Achieved in Practice |
| Ships, Auxiliary Engines | Early compliance with 13 CCR, section 2299.1 | < 0.1% Sulfur by 2010 | NA | 10% | NA | 96% | 66% | Information currently not available. | NYK Line, POLA |
| Ships, Auxiliary Engines | Alternative Marine Power (Cold Ironing) | NA | Near 100% | Near 100% | Near 100% | Near 100% | Near 100% | Information currently not available. | China Shipping, POLA, Berth 100, Princess Cruise Ships, Juneau, Alaska & Seattle, WA Land-based diesel. |
|  | Selective Catalytic Reduction retrofit with low sulfur fuel | NA | 0% | 85% | 0% | 40% | 18% | Retrofit Capital Cost SE: $423,656 ME: $985,144 LE: $2,263,880 | Engines and ship engines in Denmark and Sweden |
| Ships, Propulsion & Auxiliary Engines | Water/fuel emulsions | NA | 0% | 25% | 0% | 0% | 0% | $550,000 to $750,000 | A demonstration project is planned by the California Maritime Working Group |
|  | Emission Reduction |  |
| Emission Source | Control Technology (CT) | Date CT Required | CO | NOx | VOC | SO2 | PM | Cost | Project/Where Achieved in Practice |
| Ships, Propulsion & Auxiliary Engines | Water injection | NA | 0% | 50% | 0% | 0% | 0% | New Capital Cost SE: 169,665 ME: $338,223 LE: $686,166 Annual O&M SE: $41,488 ME: $135,700 LE: $338,750 | Propulsion engines in Denmark and Sweden |

# Footnotes

Date that control equipment is required by local, state, or federal agencies through a rule, regulation, or law.

Cost data from “Controlling Air Emissions From Marine Vessels: Problems and Opportunities” by Anthony Fournier, February 2006 (http://www.westcoastdiesel.org/files/clearinghouse-marine/Fournier%20Marine%20Emissions%20Problems%20and%20Opportunities.pdf).

POLA = Port of Los Angeles. POLB = Port of Long Beach.

Because actual NOx reduction is dependent on vessel service speed, this requires case by case evaluation. 50% is simply an estimate.

From reference cited in Footnote 2: Small Engine (3,000 kW) = $196,134; Medium Engine (10,000 kW) = $642,118; Large Engine (25,000 kW) = $1,602,796

From reference cited in Footnote 2: Small Engine (3,000 kW) = $252,171; Medium Engine (10,000 kW) = $825,580; Large Engine (25,000 kW) = $2,060,738

Date that control equipment is required by local, state, or federal agencies through a rule, regulation, or law.

Cost data from “Controlling Air Emissions From Marine Vessels: Problems and Opportunities” by Anthony Fournier, February 2006 (http://www.westcoastdiesel.org/files/clearinghouse-marine/Fournier%20Marine%20Emissions%20Problems%20and%20Opportunities.pdf).
SE = Small Engine (3,000 kW)    ME = Medium Engine (10,000 kW)    LE = Large Engine (25,000 kW)

POLA = Port of Los Angeles. POLB = Port of Long Beach.

Date that control equipment is required by local, state, or federal agencies through a rule, regulation, or law.

Cost data from “Controlling Air Emissions From Marine Vessels: Problems and Opportunities” by Anthony Fournier, February 2006 (http://www.westcoastdiesel.org/files/clearinghouse-marine/Fournier%20Marine%20Emissions%20Problems%20and%20Opportunities.pdf).
SE = Small Engine (3,000 kW)    ME = Medium Engine (10,000 kW)    LE = Large Engine (25,000 kW)

POLA = Port of Los Angeles. POLB = Port of Long Beach.

Date that control equipment is required by local, state, or federal agencies through a rule, regulation, or law.

Cost data from “Controlling Air Emissions From Marine Vessels: Problems and Opportunities” by Anthony Fournier, February 2006 (http://www.westcoastdiesel.org/files/clearinghouse-marine/Fournier%20Marine%20Emissions%20Problems%20and%20Opportunities.pdf).
SE = Small Engine (3,000 kW)    ME = Medium Engine (10,000 kW)    LE = Large Engine (25,000 kW)