SOUTH COAST AIR QUALITY MANAGEMENT DISTRICT

ASBESTOS REMOVAL AND DEMOLITION GUIDELINES

FOR STATE DECLARED EMERGENCIES

After a major fire, earthquake or wind storm, many buildings will require debris removal or demolition.  Be aware that buildings constructed prior to 1984 may have asbestos-containing materials (ACM)*.  Even buildings constructed after 1984 can contain some asbestos.  Materials that may contain asbestos include roofs, floor tiles, acoustic ceilings, insulation, sound proofing, cement pipes, heating ducts, pipe coverings and others.

To aid the disaster recovery, AQMD has streamlined its asbestos notification procedures by temporarily waiving the fees and the waiting period for cleanups in the affected areas in Los Angeles County and the city of Rancho Cucamonga resulting from the severe winds on or about November 30, 2011.

GUIDELINES FOR CLEANUP

- Avoid mixing of asbestos-containing materials with other debris.  Use adequate wetting for all debris removals and demolitions.  For wetting, use a dispenser or water hose with a nozzle for a fine, low-pressure spray or mist.  Where necessary, use water mixed with wetting agent.

- Where ACM is suspected to be mixed with debris, the debris may be assumed to be ACM and should be adequately wetted, wrapped in thick plastic sheeting (”burrito-wrapped”) and disposed of as ACM.  A survey by a certified consultant may be conducted to separate ACM from other debris in order to reduce the amount of debris that needs to be disposed of as ACM.

- Where ACM is known to be present, the debris should be stabilized by wetting and covering with plastic sheeting until it is removed.

- Suspected or known ACM must be removed by a licensed asbestos abatement contractor and disposed of at a landfill approved to receive asbestos.  Some exemptions may apply to an owner-occupant of a single-family house who plans to conduct their own cleanup.  Contact AQMD, (909) 396-2336, for details.

NOTIFICATIONS

- Contractors, owners, or operators are responsible for notifying AQMD prior to proceeding with asbestos removals and/or demolitions.  “No person shall remove or strip ACM or Class II nonfriable ACM that has suffered damage from fire, explosion, or natural disaster without the use of a Procedure 5 Approved Alternative” (Rule 1403).

- Indicate “Emergency-related” on the top of the standard notification form.  If a building has been condemned by a city or county agency, indicate this fact in the notification.

- Asbestos notification forms can be obtained from the AQMD’s website (www.aqmd.gov).or by calling (909) 396-2336.   Fax the completed form to (909) 396-3342 or mail to AQMD Asbestos Program, 21865 Copley Drive, Diamond Bar, CA 91765-4178.

- If a previously submitted notification needs revisions due to the emergency, the contractor can fax a revised notification without a fee.

- Contact the State of California, Department of Toxics Substance Control for disposal and transport of asbestos-containing materials at (818) 717-6500.

For more information call AQMD at (909) 396-2336.  For information about licensed contractors contact State Licensing Board or call AQMD.

*By definition, asbestos-containing material (ACM) is a material containing more than 1% asbestos.