|  | Emission Reduction |
| --- | --- |
| Baseline Engine Horsepower | Locomotive Category | Project/Where Achieved in Practice | Baseline Engine Model Year | Repowered / Retrofitted / New Engine | CO | NOx | VOC | SO2 | PM |
|  |  |  |  | Model Year | EPA Certification Level | Cost ($1,000) |  |  |  |  |  |
| 900 | Switcher (1) | TAMCO Steel | pre-1973 | 2005 (N) | Off-Road Tier 3 | $419 (05) | 0% | 85% | 88% | ND | 78% |
| 1200 | Switcher (3) | Pacific Harbor Line | pre-1973 | 2005 (P) | Locomotive Tier 2 | $720 (05) | 0% | 48% | 39% | ND | 39% |
| 1200 | Switcher (2) | Pacific Harbor Line | 1956 | 2003 (P) | Locomotive Tier 2 | $960 (03) | 0% | 48% | 39% | ND | 39% |
| 1200 | Switcher (3) | Pacific Harbor Line | 1957 | 2003 (P) | Locomotive Tier 2 | $960 (03) | 0% | 48% | 39% | ND | 39% |
| 1209 | Switcher (1) | AMTRAK - LA Switcher Green Goat Conversion | pre-1973 | 2005 (T) | Locomotive Tier 2 | $650 (04) | 0% | 48% | 39% | ND | 39% |
| 1500 | Switcher (1) | Pacific Harbor Line | 1950 | 2003 (P) | Locomotive Tier 2 | $960 (03) | 0% | 48% | 39% | ND | 39% |
|  | Emission Reduction |
| Baseline Engine Horsepower | Locomotive Category | Project/Where Achieved in Practice | Baseline Engine Model Year | Repowered / Retrofitted / New Engine | CO | NOx | VOC | SO2 | PM |
|  |  |  |  | Model Year | EPA Certification Level | Cost ($1,000) |  |  |  |  |  |
| 1750 | Switcher (1) | Pacific Harbor Line | 1967 | 2003 (P) | Locomotive Tier 2 | $960 (03) | 0% | 48% | 39% | ND | 39% |
| 1750 | Switcher (1) | Railserve Inc. - Green Kid | pre-1973 | 2003 (T) | Locomotive Tier 2 | $445 (03) | 0% | 48% | 39% | ND | 39% |
| 1750 | Switcher (2) | Railpower Technologies Corporation - Green Goat | pre-1973 | 2003 (T) | Locomotive Tier 2 | $770 (03) | 0% | 48% | 39% | ND | 39% |
| 1800 | Switcher (1) | Pacific Harbor Line | 1960 | 2003 (P) | Locomotive Tier 2 | $960 (03) | 0% | 48% | 39% | ND | 39% |
| 1800 | Switcher (2) | Pacific Harbor Line | pre-1973 | 2005 (P) | Locomotive Tier 2 | $720 (05) | 0% | 48% | 39% | ND | 39% |
| 1800 | Switcher (4) | Pacific Harbor Line | 1960 | 2003 (P) | Locomotive Tier 2 | $960 (03) | 0% | 48% | 39% | ND | 39% |
| 2000 | Switcher (2) | Pacific Harbor Line | 1973-2001 | 2005 (P) | Locomotive Tier 2 | $720 (05) | 70% | 42% | 71% | ND | 67% |
| 2000 | Switcher (1) | Pacific Harbor Line | 1957 | 2003 (P) | Locomotive Tier 2 | $960 (03) | 0% | 48% | 39% | ND | 39% |
|  | Emission Reduction |
| Baseline Engine Horsepower | Locomotive Category | Project/Where Achieved in Practice | Baseline Engine Model Year | Repowered / Retrofitted / New Engine | CO | NOx | VOC | SO2 | PM |
|  |  |  |  | Model Year | EPA Certification Level | Cost ($1,000) |  |  |  |  |  |
| 2000 | Switcher (1) | Pacific Harbor Line | 1963 | 2003 (P) | Locomotive Tier 2 | $960 (03) | 0% | 48% | 39% | ND | 39% |
| 2000 | Switcher (1) | Pacific Harbor Line | pre-1973 | 2003 (P) | Locomotive Tier 2 | $960 (03) | 0% | 48% | 39% | ND | 39% |
| 2000 | Switcher (1) | Pacific Harbor Line | 1967 | 2003 (P) | Locomotive Tier 2 | $960 (03) | 0% | 48% | 39% | ND | 39% |
| 2000 | Switcher (1) | Pacific Harbor Line | 1977 | 2003 (P) | Locomotive Tier 2 | $960 (03) | 70% | 42% | 71% | ND | 67% |
| 3000 | Passenger (2) | Southern California Regional Rail Authority | 1977 | 2005 (T) | Locomotive Tier 2 | $187 (04) | 70% | 42% | 70% | ND | 67% |
| 3000 | Switcher (2) | Pacific Harbor Line | 1973-2001 | 2005 (P) | Locomotive Tier 2 | $720 (05) | 70% | 42% | 71% | ND | 67% |
| 3800 | Passenger (4) | Southern California Regional Rail Authority | 1986 | 2005 (T) | Locomotive Tier 2 | $200 (04) | 70% | 42% | 70% | ND | 67% |

# Footnotes

Emission reduction is from baseline engine emission rate to specified tier emission rate (all baseline engines are Tier 0 or uncontrolled, i.e. pre-1973). Uncontrolled values are from Table B-16 (Locomotive Emission Factors), page B-16, Appendix B, of The Carl Moyer Program Guidelines, January 6, 2006 (Part II of IV - http://www.arb.ca.gov/msprog/moyer/guidelines/2005_Carl_Moyer_Guidelines_Part2.pdf). Tiered values are from Table 8-2, page VIII-3 of the same guidelines. For CEQA mitigation purposes, the lowest emission reduction must be used unless greater emission reductions can be demonstrated (e.g. manufacturer guarantee).

(1), (2), etc. refers to the number of upgraded locomotives.

Specific project or location where engine repower/retrofit or replacement with new locomotive has been achieved in practice.

(N) = New locomotive. (P) = Repowered locomotive. (T) = Retrofitted locomotive.

For informational purposes only. Cost estimates provided by project proponents. Actual costs may vary. Cost includes repowered, retrofitted, new engine(s), labor to install engine(s), and any peripheral equipment that may have been required. (03) = 2002/2003 dollars. (04) = 2003/2004 dollars. (05) = 2004/2005 dollars.

Three (3) 300 horsepower engines (= 900 horsepower total).

Old switcher locomotive replaced with new locomotive fitted with three (3) Tier 3 off-road engines, each rated at 300 horsepower. Tier 3 off-road emission factors are from Table B-12, pages B-10 to B-11, Appendix B, of The Carl Moyer Program Guidelines, January 6, 2006 (Part II of IV - http://www.arb.ca.gov/msprog/moyer/guidelines/2005_Carl_Moyer_Guidelines_Part2.pdf).

Emission reduction is from baseline engine emission rate to specified tier emission rate (all baseline engines are Tier 0 or uncontrolled, i.e. pre-1973). Uncontrolled values are from Table B-16 (Locomotive Emission Factors), page B-16, Appendix B, of The Carl Moyer Program Guidelines, January 6, 2006 (Part II of IV - http://www.arb.ca.gov/msprog/moyer/guidelines/2005_Carl_Moyer_Guidelines_Part2.pdf). Tiered values are from Table 8-2, page VIII-3 of the same guidelines. For CEQA mitigation purposes, the lowest emission reduction must be used unless greater emission reductions can be demonstrated (e.g. manufacturer guarantee).

(1), (2), etc. refers to the number of upgraded locomotives.

Specific project or location where engine repower/retrofit or replacement with new locomotive has been achieved in practice.

(N) = New locomotive. (P) = Repowered locomotive. (T) = Retrofitted locomotive.

For informational purposes only. Cost estimates provided by project proponents. Actual costs may vary. Cost includes repowered, retrofitted, new engine(s), labor to install engine(s), and any peripheral equipment that may have been required. (03) = 2002/2003 dollars. (04) = 2003/2004 dollars. (05) = 2004/2005 dollars.

Emission reduction is from baseline engine emission rate to specified tier emission rate (all baseline engines are Tier 0 or uncontrolled, i.e. pre-1973). Uncontrolled values are from Table B-16 (Locomotive Emission Factors), page B-16, Appendix B, of The Carl Moyer Program Guidelines, January 6, 2006 (Part II of IV - http://www.arb.ca.gov/msprog/moyer/guidelines/2005_Carl_Moyer_Guidelines_Part2.pdf). Tiered values are from Table 8-2, page VIII-3 of the same guidelines. For CEQA mitigation purposes, the lowest emission reduction must be used unless greater emission reductions can be demonstrated (e.g. manufacturer guarantee).

(1), (2), etc. refers to the number of upgraded locomotives.

Specific project or location where engine repower/retrofit or replacement with new locomotive has been achieved in practice.

(N) = New locomotive. (P) = Repowered locomotive. (T) = Retrofitted locomotive.

For informational purposes only. Cost estimates provided by project proponents. Actual costs may vary. Cost includes repowered, retrofitted, new engine(s), labor to install engine(s), and any peripheral equipment that may have been required. (03) = 2002/2003 dollars. (04) = 2003/2004 dollars. (05) = 2004/2005 dollars.